## Slide 1: Water Resources Engineering Lecture 10
Hydrologic Analysis-Rainfall-Runoff Estimation Methods 3
Dr. Zada Tawalbeh
Ajloun National University

## Slide 2: Rainfall-Runoff-NRCS Method
• Estimates runoff from rainfall
• Based on watershed characteristics
NRCS = Natural Resources Conservation Service
Used to estimate runoff from rainfall
Based on watershed characteristics (soil, land use, cover, slope)
Previously known as the SCS Curve Number Method

## Slide 4: Rainfall-Runoff-NRCS Method

## Slide 5: Rainfall-Runoff-NRCS Method-Metric Unit

## Slide 6: CN Depends On
• Soil type
• Land use
• Land condition
• Hydrologic soil group A–D
CN represents watershed ability to absorb water
Low CN → more infiltration → less runoff
High CN → less infiltration → more runoff
Depends on: Soil group (A, B, C, D)
Land use (urban, agriculture, forest)
Soil treatment/condition
Hydrologic condition (poor/Fair/good)
Low CN (e.g., forests, sandy soils) → water infiltrates easily
High CN (e.g., urban areas, clay soils) → water runs off quickly

## Slide 7: Soil Hydrologic Groups

## Slide 8: a) Soil Hydrologic Groups
A: high infiltration (sand) → least runoff
B: moderate infiltration
C: low infiltration
D: very low infiltration (clay) → most runoff

## Slide 10: Curve Number
Curve number CN depends upon:
a) Soil type
b) Antecedent moisture condition
c) Land use/cover

## Slide 16: Initial Abstraction (Ia)
Initial Abstraction (Ia)
Includes:
  Surface storage
  Interception
  Infiltration before runoff starts
Traditional assumption: Ia = 0.2 S (where S depends on CN)

## Slide 17: Runoff Equation
Main Runoff Equation
Q = runoff depth
P = total rainfall
S = potential maximum retention

## Slide 18: Time of Concentration (Tc)
Time of Concentration (Tc)
The time required for water to travel from the farthest point in watershed to outlet
Determines hydrograph peak time
Depends on:
  Slope
  Surface roughness
  Flow path length
  Land use

## Slide 19: Summary: NRCS Unit Hydrograph
Watershed Response (Hydrograph)
NRCS uses dimensionless unit hydrograph
Need:
  Excess rainfall
  Time of concentration
  Watershed area
Produces:
  Peak discharge
  Runoff volume
  Hydrograph shape

## Slide 20: Example 1:
A semi-arid watershed has a total area of 150 ha. The land cover types and hydrologic soil groups are given below (assume AMC-II conditions and ).
Use Table 2-2c (other agricultural lands) and Table 2-2d (arid and semiarid rangelands) to select the CNII values for each land cover and soil group.
A storm produces a rainfall depth of mm.
1. Determine the composite Curve Number for the watershed.
2. Compute:
S (mm)
𝐼𝑎 (mm)
Runoff depth 𝑄(mm) using the SCS runoff equation.

## Slide 21
Land cover type (from tables) | Hydrologic condition | Soil group | Area (ha)
Pasture, grassland, or range (continuous grazing) | Good | C | 40
Brush (brush-weed-grass mixture) | Fair | B | 30
Desert shrub | Poor | D | 50
Woods | Good | B | 20
Farmsteads (buildings, lanes, driveways, lots) | — | C | 10

## Slide 22: Solution
Land cover | Area (ha) | CN
Pasture (Good, C) | 40 | 74
Brush (Fair, B) | 30 | 56
Desert shrub (Poor, D) | 50 | 88
Woods (Good, B) | 20 | 55
Farmsteads (C) | 10 | 82

## Slide 25: Example 2:
A watershed has a total area of 100 ha with the following land uses:
Land Use (from Table 4-a) | Hydrologic condition / practice | Soil group | Area (ha)
Cultivated – Contoured | Good | C | 30
Forest | Open | B | 25
Pasture | Fair | D | 20
Roads (dirt) | — | C | 15
Hard surface areas | — | D | 10
A storm produces a rainfall depth of . Assume and AMC-II.
Find:
Composite Curve Number
mm), mm), and runoff depth (mm)

## Slide 26: Solution
Land Use | Treatment / Condition | Hydrologic Soil Group | Curve Number (CN)
Cultivated land | Contoured (Good) | C | 82
Forest | Open | B | 44
Pasture | Fair | D | 84
Roads (dirt) | — | C | 88
Hard surface areas | — | D | 93

## Slide 29: Example3
A watershed has a total area of 120 ha. The land use, condition/practice, soil group, and areas are:
Land Use (Table 4-a) | Treatment / Condition | Hydrologic Soil Group | Area (ha)
Cultivated | Contoured & Terraced (Poor) | B | 30
Cultivated | Bunded (Good) | C | 25
Orchards | With understory cover | D | 15
Forest | Dense | A | 20
Pasture | Good | B | 20
Roads (dirt) | — | D | 10
Find CN from Table (4-a) and Compute Composite CN