## Slide 1: Chapter 6 Memory

## Slide 2: Lecture Overview
Introduction to this Lecture's activities
In this lecture, you will learn about memory and its organization. This lecture covers basic memory concepts, such as RAM and the various memory devices, and addresses the more advanced concepts of the memory hierarchy, including cache memory.
In addition, you will learn about some types of cache mapping schemes, and their influence on the performance of the whole computer system. This lecture gives a thorough presentation of direct mapping, associative mapping, and set-associative mapping techniques for cache.

## Slide 3: Lecture Overview
Introduction to this Lecture's activities
After completing the lecture, you will be able to:
Describe the concepts of hierarchical memory organization.
Illustrate how each level of memory contributes to system performance.
Identify the concepts behind cache memory, and address translation.
Demonstrate how each cache scheme contributes to system performance.

## Slide 4: Lecture Overview
Introduction
Types of Memory
The Memory Hierarchy
Cache Memory

## Slide 5: Introduction
Most computers are built using the Von Neumann model, which is centered on memory. The programs that perform the processing are stored in memory. Memory lies at the heart of the stored-program computer.
In previous lectures, you have studied the components from which memory is built, and the ways in which memory is accessed by various ISAs.
In the remaining sections, the focus will be on memory organization. You will examine the various types of memory, and the way each is part of the memory hierarchy system. You will then have a look at the cache memory (a special high-speed memory) and the mapping schemes used.
A clear understanding of these ideas is essential for the analysis of system performance.

## Slide 6: Lecture Overview
Introduction
Types of Memory
The Memory Hierarchy
Cache Memory

## Slide 7: Types of Memory
A common question many people ask is “why are there so many different types of computer memory?”
New technologies continue to be introduced in an attempt to match the improvements in CPU design.
The speed of memory has to, somewhat, keep pace with the CPU, or the memory becomes a bottleneck.

## Slide 8: Types of Memory
There are two kinds of main memory
Random access memory: RAM
Read-only-memory: ROM
RAM
RAM is a read-write memory.
RAM is the memory to which computer specifications refer; if you buy a computer with 4GB of memory, it has a 4GB of RAM.
RAM is also the “main memory” we have continually referred to throughout this text.
RAM is used to store programs and data that the computer needs when executing programs.
RAM is volatile: it loses data once the power is turned off.
There are two general types of RAM memory in today’s computers: DRAM and SRAM

## Slide 9: Types of Memory
Dynamic RAM – DRAM:
DRAM is constructed of tiny capacitors that leak electricity.
DRAM requires a recharge every few milliseconds to maintain its data.
Advantages of DRAM
  It is much denser (can store many bits per chip),
  uses less power,
  less expensive,
  Slower than SRAM
  generates less heat than SRAM
Static RAM – SRAM
SRAM holds its contents as long as power is available (No need for recharge).
SRAM consists of circuits similar to the D flip-flops.
SRAM is faster.
SRAM is much more expensive than DRAM.
SRAM smaller than DRAM
Both technologies, DRAM and SRAM, are often used in combination: DRAM for main memory and SRAM for cache.

## Slide 10: Types of Memory
ROM
ROM stores critical information necessary to operate the system, such as the program necessary to boot the computer.
ROM is not volatile and always retains its data.
This type of memory is also used in embedded systems or any systems where the programming does not need to change.
Examples of Systems that uses ROM: Toys, Automobiles, calculators, printers, etc.
There are five basic different types of ROM: ROM, PROM, EPROM, EEPROM, and flash memory.

## Slide 11: Types of Memory
PROM (programmable read-only memory)
  PROMs can be programmed by the user with the appropriate equipment.
  Whereas ROMs are hardwired, PROMs have fuses that can be blown to program the chip.
  Once programmed, the data and instructions in PROM cannot be changed.
EPROM (erasable PROM)
  EPROM is programmable and reprogrammable
  Erasing an EPROM requires a special tool that emits ultraviolet light.
  To reprogram an EPROM, the entire chip must first be erased.
EEPROM (electrically erasable PROM)
  No special tools are required for erasure
  Erasure is performed by applying an electric field
  Only portions of the chip can be erased, one byte at a time.
Flash memory
  Flash memory is essentially EEPROM
  It can be written or erased in blocks, removing the one-byte-at-a-time limitation.
  Flash memory is faster than EEPROM.

## Slide 12: Lecture Overview
Introduction
Types of Memory
The Memory Hierarchy
Cache Memory

## Slide 13: The Memory Hierarchy
One of the most important considerations in understanding the performance capabilities of a modern processor is the memory hierarchy. Unfortunately, not all memory is created equal, and some types are far less efficient and thus cheaper than others.
As a rule, the faster memory is, the more expensive it is per bit of storage.
To deal with this disparity, today’s computer systems use a combination of memory types to provide the best performance at the best cost. This approach is called Hierarchical Memory.
The base types that normally constitute the hierarchical memory system include:
Registers, cache, main memory, and secondary memory.

## Slide 14: The Memory Hierarchy
We classify memory based on its “distance” from the processor.
Distance is usually measured by the number of machine cycles required for access. The closer memory is to the processor, the faster and smaller it should be.
Faster memory is more expensive. Thus, faster memories tend to be smaller than slower ones, due to cost.
In todays’ computers:
Memories close to the CPU are high speed, low capacity memories (i.e. cache memory)
Memories far from the CPU are low speed high capacity memories (i.e. Hard Disk)
In between comes the main RAM memory.

## Slide 15: The Memory Hierarchy
The Memory hierarchy is depicted in figure 6.1:
Figure ‎6.1: Memory Hierarchy

## Slide 16: The Memory Hierarchy
To access a particular piece of data:
The CPU first sends a request to its nearest memory, usually cache.
If the data is not in cache, then main memory is queried.
If the data is not in main memory, then the request goes to disk.
Once the data is located, then the data, and a number of its nearby data elements are fetched into cache memory.

## Slide 17: The Memory Hierarchy
This leads us to some definitions:
  A Hit: is when data is found at a given memory level.
  A Miss: is when it is not found.
  The Hit Rate: is the percentage of time data is found at a given memory level.
  The Miss rate: is the percentage of time it is not.
  Note that: Miss rate = 1 - Hit Rate.
  The Hit Time: is the time required to access data at a given memory level.
  The miss penalty: is the time required to process a miss, including the time that it takes to replace a block of memory plus the time it takes to deliver the data to the processor.

## Slide 18: The Memory Hierarchy
CPU
RAM
Hard Disk Drive
HDD
Data address X
Data address
X
Data address
X
Data at addresses
X, X+1, X+2 …
Data at addresses
X, X+1, X+2 …
Data at
address X
Data block 1
Data block 2
Data at location X
Miss!
Miss!
Hit!
Cache
Figure 6.2 shows the process of seeking (in RED) and getting the needed data (in Green):
Figure 6.2: Seeking and getting data

## Slide 19: The Memory Hierarchy
“Once the data is located, then the data, and a number of its nearby data elements are fetched into cache memory”. Why?
  The hope is that this extra data will be referenced in the near future, which, in most cases, it is.
    Why?
      because programs tend to exhibit a property known as locality.
  Advantage: After a miss, there is a high probability to achieve several hits .
Although there is one miss on, there might be several hits in cache on the newly retrieved block afterward, due to locality.
The CPU requests the content of location X from cache memory and the result is a Miss.
The request goes to lower levels, until a Hit is recorded. The result is a block of data that is transferred from the component that has the needed data to the previous component, until it is placed in the cache memory (the content of X, X+1, X+2 …)

## Slide 20: The Memory Hierarchy
Locality of Reference
Locality of Reference is a way of organizing data inside memory in such a way that data nearly requested will be closely located inside the memory.
“Once the data is located, then the data, and a number of its nearby data elements are fetched into cache memory”. This is because of the hope that this extra data will be referenced in the near future, which, in most cases, happens since programs tend to exhibit a locality property.
The Advantage is that after a Miss, there is a high probability to achieve several Hits.
Example: In the absence of branches, the PC in MARIE is incremented by one after each instruction fetch.
Thus, if memory location X is accessed at time t, there is a high probability that memory location X + 1 will also be accessed in the near future.
This clustering of memory references into groups is an example of locality of reference.

## Slide 21: The Memory Hierarchy
There are three forms of locality:
Temporal locality: Recently-accessed data elements tend to be accessed again.
Spatial locality: Accesses tend to cluster.
Sequential locality: Instructions tend to be accessed sequentially.
The locality principle provides the opportunity for a system to use a small amount of very fast memory to effectively accelerate the majority of memory accesses.
Typically, only a small amount of the entire memory space is being accessed at any given time, and the values from a slower memory to a smaller but faster memory that resides higher in the hierarchy.
This results in a memory system that can store a large amount of information in a large but low-cost memory, yet provide nearly the same access speeds that would result from using the fast but expensive memory.

## Slide 22: Lecture Overview
Introduction
Types of Memory
The Memory Hierarchy
Cache Memory
  Introduction
  Cache Mapping Schemes
    Direct mapping
    Fully associative
    Set Associative

## Slide 23: Cache Memory-Introduction
A computer processor is very fast and is constantly reading information from memory.
It often has to wait for the information to arrive, because the memory access times are slower than the processor speed.
A cache memory is a small, temporary, but fast memory that the processor uses for information it is likely to need again in the very near future.
Hence, the purpose of cache memory is to speed up accesses by storing recently used data closer to the CPU, instead of storing it in main memory.
Although cache is much smaller than main memory, its access time is a fraction of that of main memory.

## Slide 24: Cache Memory-Introduction
Unlike main memory, which is accessed by address, cache is typically accessed by content; hence, it is often called content addressable memory. Because of this, a single large cache memory isn’t always desirable— it takes longer to search.
Accessing data inside the cache memory is faster than accessing the same data from the main memory
Therefore, frequently used data are copied into the cache memory.
While main memory is typically composed of DRAM with, say, a 60ns access time, cache is typically composed of SRAM, providing faster access with a much shorter cycle time than DRAM. A typical cache access time is 10ns.
Moreover, if the data has been copied to cache, the address of the data in cache is not the same as the main memory address.
For example, data located at main memory address 2E3 could be located in the very first location in cache.

## Slide 25: Cache Memory-Introduction
How, then, does the CPU locate data when it has been copied into cache?
The CPU uses a specific mapping scheme.
A mapping Scheme “converts” the main memory address into a cache location.
It gives special significance to the bits in the main memory address.
We first divide the bits into distinct groups we call fields.
Depending on the mapping scheme, we may have two or three fields.
It determines where the data is placed when it is originally copied into cache.
It also provides a method for the CPU to find previously copied data when searching cache.

## Slide 26: Cache Mapping Schemes
Before we discuss mapping schemes, it is important to understand how data is copied into cache.
  Main memory and cache are both divided into the same size blocks (the size of these blocks varies).
  When a memory address is generated, cache is searched first to see if the required word exists there.
  When the requested word is not found in cache, the entire main memory block in which the word resides is loaded into cache.
You should note that:
  The main memory is bigger than cache
  So, there are more blocks in main memory than there are in cache blocks!
  Main memory blocks compete for cache locations!

## Slide 27: Cache Mapping Schemes – Direct Mapped Cache
Direct mapped cache assigns cache mappings using a modular approach.
If X is the location of a block in main memory, Y is the location of this block in cache, and N is the total number of blocks in cache, X and Y are related by the equation:
Y = X mod N
Note: Y is the remainder of the division: X/N
Example: A cache memory contains 10 blocks. How will the following main memory blocks: 0, 6, 10, 15, 25, 32 be mapped to the cache?
Here N=10 (starting from block 0 till block 9)
Block 0 will be placed in cache block: 0 mod 10 = 0
Block 6 will be placed in cache block: 6 mod 10 = 6
Block 10 will be placed in cache block: 10 mod 10 = 0
Block 15 will be placed in cache block: 15 mod 10 = 5
Block 25 will be placed in cache block: 25 mod 10 = 5
Block 32 will be places in cache block: 32 mod 10 = 2
1) Direct Mapped Cache

## Slide 28: Cache Mapping Schemes – Direct Mapped Cache
In the last example, blocks 5, 15, 25, 35, … are all placed in Block 5 in cache!
How does the CPU know which block actually resides in cache block 5 at any given time?
A tag identifies each block that is copied to cache.
This tag is stored with the block, inside the cache.
A valid bit is also added to each cache block to identify its validity.

## Slide 29: Cache Mapping Schemes – Direct Mapped Cache
To perform direct mapping, the binary main memory address is partitioned into three fields:
Offset (Word) field
  Uniquely identifies an address within a specific block (a unique word)
  The number of words/bytes in each block dictates the number of bits in the offset field
Example: If a block of memory contains 8=23 words, we need 3 bits in the offset
field to identify (address) one of these 8 words in the block (07).
Block field
  It must select a unique block of cache
  The number of blocks in cache dictates the number of bits in the block field
Example: If a cache contains 16=24 blocks, we need 4 bits to identify (address)
one of these 16 blocks.
Tag field
  Whatever is left over!
  Do not forget that: when a block of memory is copied to cache, this tag is stored with the block and uniquely identifies this block.

## Slide 30: Cache Mapping Schemes – Direct Mapped Cache
Example 1: Assume a byte-addressable memory consists of 214 bytes, cache has 16 blocks, and each block has 8 bytes. How many bits do we have in the tag, block and offset fields?
  The number of memory blocks are: 214/8 = 214/23=211 blocks
  Each main memory address requires 14 bits. These are divided into three fields as follows:
    We have 8 = 23 words in each block so we need 3 bits to identify one of these words: the rightmost 3 bits reflect the offset field.
    We have 16=24 blocks in cache. We need 4 bits to select a specific block in cache, so the block field consists of the middle 4 bits.
    The remaining 7 bits make up the tag field (14 – (4 + 3)).
Figure 6.3: Explanation of each field in Direct Mapping

## Slide 31: Cache Mapping Schemes – Direct Mapped Cache
Example 2: Suppose a computer using direct mapped cache has 220 words of main memory, and a cache of 32 blocks, where each cache block contains 16 words.
a. How many blocks of main memory are there?
b. What is the format of a memory address as seen by the cache, i.e., what are the sizes of the tag, block, and word fields?
c. To which cache block will the memory reference 0DB6316 map?
Answer:
a. 220/16 = 220/24 = 216 blocks
b. 20 bit addresses with 11 bits in the tag field, 5 in the block field, and 4 in the word field
32 blocks = 25 11 bits 5 bits 4 bits
16 words = 24
Tag = 20 – (4+5) = 11
c. 0DB63 = 00001100101 10110 0111, which is Block 22
0000 1101 1011 0110 0011

## Slide 32: Cache Mapping Schemes – Direct Mapped Cache
Summary:
  Direct mapped cache maps main memory blocks in a modular fashion to cache blocks. The mapping depends on:
    The number of bits in the main memory address (how many addresses exist in main memory)
    The number of blocks are in cache (which determines the size of the block field)
    How many addresses (either bytes or words) are in a block (which determines the size of the offset field)

## Slide 33: Cache Mapping Schemes – Direct Mapped Cache
Summary:
  Direct mapped cache is not as expensive as other caches because the mapping scheme does not require any searching.
    Each main memory block has a specific location to which it maps in cache.
    A main memory address is converted to a cache address.
    The block field identifies one unique cache block.
    The CPU knows “a priori” the cache block number in which it may find needed data.

## Slide 34: Cache Mapping Schemes – Fully associative Cache
In a fully associative cache scheme, a main memory block can be placed anywhere in cache.
The only way to find a block mapped this way is to search all of cache!
This requires the entire cache to be built from associative memory so it can be searched in parallel.
A single search must compare the requested tag to ALL tags in cache to determine whether the desired data block is present in cache.
Associative memory requires special hardware to allow associative searching, and is, thus, quite expensive.
2) Fully associative Cache

## Slide 35: Cache Mapping Schemes – Fully associative Cache
Using associative mapping, the main memory address is partitioned into two pieces, the tag and the word (offset).
As for direct mapped cache, the tag must be stored with each block in cache.
The word (offset) specifies a given word in the block.
Figure 6.4 shows the general format of the fully associative mapping scheme.
Figure 6.4: Fully associative format

## Slide 36: Cache Mapping Schemes – Fully associative Cache
Example 1: For a memory configuration with 214 words, and fully associative cache with 16 blocks, and blocks of 8 words:
Answer:
We have 8=23 words in each block. The word (offset) field consists of 3 bits.
The tag field is 11 bits.
Figure 6.5: Detailed format of example 1

## Slide 37: Cache Mapping Schemes – Fully associative Cache
Example 2: Suppose that a computer using fully associative cache has 216 words of main memory and a cache of 64 blocks, where each cache block contains 32 words.
a. How many blocks of main memory are there?
b. What is the format of a memory address as seen by the cache, i.e., what are the sizes of the tag and word fields?
To which cache block will the memory reference F8C9 map?
Answer:
Memory blocks = 216/32 = 216/25 = 211 .
16 bit addresses with 11 bits in the tag field and 5 in the word field.
Since it is associative cache, it can map anywhere.
Figure 6.6: Detailed format of example 2

## Slide 38: Cache Mapping Schemes – Fully associative Cache
With direct mapping, if a block already occupies the cache location where a new block must be placed, the block currently in cache is removed
  It is written back to main memory if it has been modified or simply overwritten if it has not been changed.
With fully associative mapping, when cache is full, we need a replacement algorithm to decide which block we wish to throw out of cache
  We call this our victim block.
  Examples of Replacement algorithms: Least recently used (LRU), First In First Out (FIFO).

## Slide 39: Cache Mapping Schemes – Set associative Cache
Why moving to set-associative mapping scheme?
  Fully associative is not restrictive. It allows a block from main memory to be placed anywhere.
    However, it requires a larger tag to be stored with the block (which results in a larger cache)
    It requires special hardware for searching of all blocks in cache simultaneously (which implies a more expensive cache).
  Set associative cache mapping is a scheme somewhere in the middle.
  Set associative cache mapping is a combination of direct and associative mapping schemes
    It takes the advantages of direct-mapping (low cost) and fully-associative (not restrictive)

## Slide 40: Cache Mapping Schemes – Set associative Cache
Set associative cache mapping is a combination of direct and associative mapping schemes.
It takes the advantages of direct-mapping (low cost) and fully-associative (not restrictive).
How does the N-way set associative cache mapping scheme work?
The cache memory is divided into sets of N blocks
Instead of mapping to a single cache block (as in direct-mapping scheme), an address maps to a set of N blocks in cache
Once the desired set is located, the cache is treated as associative memory
  The tag of the main memory address is compared to the tags of each valid block in the set.
3) Set associative Cache

## Slide 41: Cache Mapping Schemes – Set associative Cache
In set-associative cache mapping, the main memory address is partitioned into three pieces: the tag field, the set field, and the word field.
The tag and word (offset) fields assume the same roles as before.
The set field indicates into which cache set the main memory block maps.
Figure 6.7 shows the general format of the fully associative mapping scheme.
Figure 6.7: N-way Set Associative format
For example, a 2-way set associative cache can be conceptualized as shown in figure 6.8.
Figure 6.8: Set associative logical View

## Slide 42: Cache Mapping Schemes – Set associative Cache
Example 1: A main word addressable memory contains 214 words. A cache contains 16 blocks, where each block contains 8 words. Show how the main memory address is partitioned if the system uses 2-way set associative mapping scheme.
Answer:
A memory address is composed of 14 bits.
The cache consists of a total of 16 blocks, and each set has 2 blocks ( since we are using 2-way)
The number of sets in cache is: 16/2 = 8 sets
To address one of the 8=23 sets we need 3 bits. Therefore, the set field is 3 bits
Each block contains 8=23 words, so the word field is 3 bits.
The remaining 14-(3+3) = 8 bits creates the tag field.
Figure 6.9: Detailed format of example 1

## Slide 43: Cache Mapping Schemes – Set associative Cache
Example 2: Assume a system’s memory has 64M words. Blocks are 64 words in length and the cache consists of 16K blocks. Show the format for a main memory address assuming a 4-way set associative cache mapping scheme. Be sure to include the fields as well as their sizes.
Answer:
Memory size = 64M = 26 210 210 = 226 So, each address has 26 bits
Block size = 64 = 26 So, 6 bits in the word field
Number of sets = 16k /4 (since 4-way) = 4k = 22 210 = 212
So, 12 bits for the set field
and there are 8 bits in the tag field (26 – (12+6))
Figure 6.10: Detailed format of example 2

## Slide 44: All-in-one Example
To wrap up things, let us have an example that covers the three schemes.
Example:
Suppose a byte-addressable memory contains 1MB and the cache consists of 32 blocks, where each block contains 16 bytes.
Using the schemes below, specify their different fields, and determine where the main memory address 326A016 maps to in cache by specifying either the cache block or cache set:
A direct mapping scheme is used.
A fully associative mapping scheme is used.
A 4-way set associative mapping scheme is used.

## Slide 45: Example - Solution
Direct mapping:
  Memory size = 1M = 1. 210 210 = 220 So, each main memory address requires 20 bits.
  These are divided into three fields as follows:
    We have 16 = 24 words in each block so we need 4 bits to identify one of these words: the rightmost 4 bits reflect the offset field.
    We have 32=25 blocks in cache. We need 5 bits to select a specific block in cache, so the block field consists of the middle 5 bits.
    The remaining 11 bits make up the tag field.
  The address 326A0 maps to cache block 01010 (block A16=1010)

## Slide 46: Example - Solution
Fully associative:
    We have 16 = 24 words in each block so we need 4 bits to identify one of these words: the rightmost 4 bits reflect the offset field.
    The remaining 16 bits make up the tag field.
    We cannot determine to which cache block the memory address 326A0 maps. The address can map anywhere in cache: The whole cache needs to be searched before the desired data could be found (by comparing the tag in the address to all tags in cache).

## Slide 47: Example - Solution
4-way set associative:
We have 16 = 24 words in each block so we need 4 bits to identify one of these words: the rightmost 4 bits reflect the offset field.
The cache consists of a total of 32 blocks, and each set has 4 blocks ( since we are using 4-way)
The number of sets in cache is: 32/4 = 8 sets
To address one of the 8=23 sets we need 3 bits. Therefore, the set field is 3 bits
The remaining 20-(4+3) = 13 bits creates the tag field.
The main memory address 326A0 maps to cache set 0102 = 210. We cannot know which block in the set is addressed, the set still needs to be searched before the desired data could be found (by comparing the tag of the address to all tags in cache set 2)

## Slide 48: End of chapter 6 Try to solve all exercises related to chapter 6 Good Luck on your Final Exam!